## Slide 1: Quantum linear solvers for fluid dynamics
Murali Gopalakrishnan Meena
OLCF, Oak Ridge National Laboratory
WCISCC 2025 ORNL
This research used resources of the Oak Ridge Leadership Computing Facility (OLCF) at the Oak Ridge National Laboratory, which is supported by the Office of Science of the U.S. Department of Energy under Contract No. DE-AC05-00OR22725.

## Slide 2: Introduction & Motivation
Fluid dynamics & Linear system of equations

## Slide 3: Fluid dynamics is everywhere & its “pretty” turbulent
[1] Gopalakrishnan Meena, et al., PRE, 2018
[2] Gopalakrishnan Meena & Taira, J. Fluid Mech., 2021
Community structures in 3D isotropic turbulence[2]
Reduce-order modeling of laminar flow over an airfoil[1]

## Slide 4: Governing equations of fluid flow comprise of linear & nonlinear terms that can be solved numerically
Conservation of mass
Conservation of momentum
Pressure Poisson equation
The Navier—Stokes Equations

## Slide 5: Governing equations are discretized to create a set of algebraic equations & assembled into
Linear Solver

## Slide 6: Grid resolution can get prohibitively expensive to simulate for practical fluid flow problems
Contour plot of the perturbed vertical density gradient for 1/4th of the domain.
3D stratified turbulence model for oceanographic flow[1]
grid points
Turbulence related projects: 35-45% of 2023 OLCF Frontier allocation
Isosurface of scalar dissipation rate for 1/25th of the domain, constructed using triangles.
[1] J. J. Riley, et al., J. Turbulence, 2023
Contour plots of the perturbed density after subsampling the domain.

## Slide 7: Quantum linear solvers have the potential to exponentially reduce cost of solving large problems
Quantum computing applications to fluid flow problems:
  Lattice simulations: fluid motion modeled as the motion of discrete particles
  Continuum simulations: fluid motion modeled as a continuous field
Ideal or linearized fluid flow problems: N—S equations with assumptions
  Governing equations for many can be represented as a system of linear equations - use Quantum Linear System Algorithms (QLSA)!![1-4]
  Compare the computational cost of sparse linear solvers
    Classical: (or higher for denser non-symmetric matrices)
    Quantum:
[1] Yepez, PRE, 2001
[2] Xu, Daley, Givi, Somma, AIAAJ, 2018
[3] Bharadwaj & Sreenivasan, PNAS, 2023
[4] Gopalakrishnan Meena at al., PoF, 2024
Notes: Ideal flow – forms basis for modeling many real world flow problems (some have direct practical implications)

## Slide 8: Objectives of this presentation
Disclaimer: We are not trying to show/demonstrate quantum advantage for fluid flow problems
Current talk objectives:
  Preliminary efforts at OLCF to investigate the application of QLSA on canonical fluid flow problems[1]
  Practical issues on using the algorithms for canonical fluid flow problems
    Accuracy
    Computational cost
    Noise modeling & mitigation
    Running on real hardware
[1] Gopalakrishnan Meena at al., PoF, 2024

## Slide 9: Quantum Computing
A very brief Intro to QC

## Slide 10: Classical vs Quantum Computing
Bit vs Qubit – information states
State of superposition – a combination of all possible configurations
  Store more information!
  Measuring will lead to collapse to a binary state
Types of qubits:
  Superconducting
  Trapped ion
  Photons
  Neutral atoms
  Quantum dots
https://www.ibm.com/think/topics/quantum-computing
Classical computing - Bit
Quantum computing - Qubit
Quasi-probabilities
Notes: Perform calculations exponentially faster w.r.t the input size
Simulations in chemistry & materials, cryptography, search, ML

## Slide 11: Key principles of quantum computing
Superposition
Entanglement – ability of qubits to correlate with each others’ states
  Store even more information!
Interference – information is structured like waves with amplitudes
  Waves can amplify or cancel each other
  Amplitudes: Probabilities of the outcomes of measurement
Decoherence – collapse from quantum to nonquantum state
  Intentionally (measurement)
  Allows quantum computers to interact with classical computers
  Unintentionally (interaction with environment)
Qubit
Classical Bit
Quasi-probabilities

## Slide 12: Working of a quantum computer
Qubits are prepared as superposition of states
Gates used to operate on qubits and entangle them
  Unitary operations
  Reversible
  Can operate on a single qubit or multiple (entanglement)
Circuits are collection of gates
Quantum algorithms are collection of circuits to create desired interference between states
Measurement (amplified outcomes) gives solution
Phase Estimation
Inverse Phase Estimation

## Slide 13: Running a quantum algorithm
Backend | Mechanism | Functionality
Simulator | Classical | Classical program modeling a quantum system in an ideal scenario
Emulator | Classical | Classical program modeling actual behavior of a quantum system
Real | Quantum | Physical hardware performing real quantum computations

## Slide 14: QLSA + Fluid Dynamics
Solving the Hele—Shaw flow using QLSA

## Slide 15: Model problem: Hele—Shaw flow
Flow between 2 flat plates driven by pressure difference at inlet & outlet
Flow properties:
  2D, Steady
  Incompressible, inviscid
N—S equations reduce to
  and
Decoupling pressure & velocity converts the problem into the form 𝐴𝒙=𝒃

## Slide 16: Overview of solving the Hele—Shaw flow using a QLSA

## Slide 17: The Harrow–Hassidim–Lloyd (HHL) algorithm
Convert the problem using eigen basis of Hermitian to give
  , & are the eigenvalues & eigenvectors of
  Usually, since fluid flow Jacobians are not usually Hermitian
  Use Quantum Phase Estimation (QPE) to obtain eigen basis
  Computational complexity: , – size of , – sparsity of , – condition number of , – accuracy of approximation
Current implementation using Qiskit
Harrow, Hassidim, and Lloyd, PRL, 2009
Zaman et al., IEEE Access, 2023

## Slide 18: Results: Accurate reconstruction of the pressure & velocity profiles achieved using simulators
Variable | Pressure | Velocity
Fidelity (%) | 99.9 | 99.9
Results using classical simulators

## Slide 19: Results: Computational costs are quite high attributing to condition number of system
Testing a sample system of linear equations: tridiagonal Toeplitz matrix
  Need for GPU accelerated simulators: cuQuantum
  Preconditioning matrix or preconditioning-free HHL algorithm
  Better QPE algorithm

## Slide 20: Results: Noise modeling, error mitigation & suppression better enable running on real hardware
Noise modeling & mitigation using Qiskit primitives: Sampler
Noise model: fake backends
Error mitigation: qubit readout errors
Error suppression: Optimizing circuit and Dynamic decoupling
* Gopalakrishnan Meena at al., PoF, 2024

## Slide 21: Future directions
Computational cost
  Need for hybrid quantum-classical algorithms[1,2,3]: Variational Quantum Linear Solvers
  Enhanced QPE algorithm
Error modeling & mitigation for real hardware
  Better/additional noise model
  Other mitigation strategies (relevance of Estimator)
  Different hardware (eliminating swap gates) – trapped ion (Quantinuum, IonQ)
Tackle more complex flow problems
  2D potential flow over a cylinder/sphere
[1] Bravo-Prieto et al, 2020
[2] Jaksch et al, AIAAJ 2023
[3] Bharadwaj & Sreenivasan, 2023

## Slide 22
Computational resource allocation at Oak Ridge Leadership Computing Facility (OLCF)
Large allocations: INCITE & ALCC
  Call for proposals: Once per year
Small allocations: DD
  Call for proposals: At any time
Frontier: World’s 1st exascale supercomputer
Quantum Computing User Program (QCUP)
Premium access to current stack of quantum devices available through OLCF
Apply any time
Each project is assigned a liaison:
  ORNL point of contact with quantum science expertise
Access available for international (non-US) participants
Contact – gopalakrishm@ornl.gov
Link
Link